## Slide 1: Mechanical Workshop
FIRST
Mid Atlantic Region
January 2016

## Slide 2: About Us
Megan Flynn
  Junior at Somerville High School
  Team 102
  Mechanical Lead and President
Doug Evans
  Freshman at Rowan University
  Team 102 alumni
  Former Mechanical Sub lead
Mechanical Workshop

## Slide 3: Robot Humor
What did the operator say when his robot died?
(ready for the answer…..)
Mechanical Workshop

## Slide 4
RUST IN PEACE !
Notes: Hopefully, with solid engineering designs and some luck, your robots will not suffer the same fate

## Slide 5: Topics
Design Process/ Build
Components
Safety
Lessons Learned
Passing Mechanical Inspection
Mechanical Workshop

## Slide 6: Design Process
Engineering Design
  The creation of plans for machines, structures, or processes to perform desired function (within a given time constraint)
Concept Development
  Brain Storming
    No bad ideas
    Mentors guide team through the process
    Mentors address issues
Mechanical Workshop
Notes: Students asked me to define engineering design
A design needs to start from a concept

## Slide 7: Design Process (cont.)
Design Approaches
  Detail Design (CAD, 3D Model)
    Requires programming knowledge
    More up front time (may save time during build)
  Hand Drawings
    Requires drafting knowledge
    Should be to scale
    Simple models can help
Mechanical Workshop
Notes: Hand Drawings – Stress making a scaled model out of cardboard, pop cycle sticks, etc. Should have movement

## Slide 8: Sample Drawing
Mechanical Workshop
Notes: I build a cardboard model based on a tennis ball, to determine how to pick up the ball and possible shot it

## Slide 9: Design Process (cont.)
Design Approaches (cont.)
  “Seat of your pants”
    Just go at it
    See what works
Build
  Build a prototype
    Use simple materials (like wood), then permanent materials
    Test, make changes, retest
Mechanical Workshop

## Slide 10: Motors (DC)
The torque generated by the motor and its speed or rotation are dependent on each other
This is a basic characteristic, it is a linear relationship
The motor will not operate at its no load speed, the required torque will determine the speed
Mechanical Workshop

## Slide 11: Motors (cont.)
Motor Example
  CIM Model FR801-001 Performance, 12V
    No Load RPM = 5310 (+/- 10%)
    Free Load Current = 2.7 Amps
    Max Power = 337 Watts (at 2655 RPM, 172 oz-in)
    Stall Torque = 343.4 oz-in
    Stall Current = 133 Amps
  Using this and other data, spreadsheet/curves can be generated
Mechanical Workshop
Notes: Information obtained directly from the AndyMark website
The other data was from the drawing on the AndyMark website

## Slide 12: Motors (cont.)
Chart: Speed vs Torque, CIM DC Motor
| 5310 | 4614 | 4320 | 3764 | 2655 | 2218 | 671 | 0
Series1 | 0 | 45 | 64 | 100 | 171.7 | 200 | 300 | 343.4
Speed vs. Torque Curve
Mechanical Workshop

## Slide 13: Motors (cont.)
Condition | Torque Oz-in | Speed RPM | Current Amps | Power Out Watts | Efficiency %
No Load | 0 | 5310 | 2.7 | 0 | 0
@ Max Eff | 45 | 4614 | 19.8 | 154 | 65
Normal Load | 64 | 4320 | 27.0 | 205 | 63
 | 100 | 3764 | 40.5 | 279 | 57
@ Max Power | 171.7 | 2655 | 67.9 | 337 | 41
 | 200 | 2218 | 79.0 | 328 | 35
 | 300 | 671 | 117.0 | 149 | 11
@ Stall | 343.4 | 0 | 133.0 | 0 | 0
Performance Data
Note efficiency increase and decrease
Mechanical Workshop
Notes: Data at 100, 200 and 300 oz-in:
Speed obtained from speed/torque plot
Current obtained from torque/current plot
Power Out (Watts) = Torque x Speed x 0.00074
Example at Max Eff.
45 x 4614 x 0.00074 = 153.6 or 154 watts
Efficiency = Power out/Power In
Example, at Max Eff.
19.8 amps x 12 volts = 237.6 watts
(154/237.6)x100 = 65%

## Slide 14: Motors (cont.)
Useful Motor Information
  Power (Watts) = Torque (oz-in) * Speed (RPM) * 0.00074
  Variation, Input Voltage
    Speed and Torque increase or decrease by the same percentage as the variation in supply voltage
    Output power increases or decreases by the following:
      (1 + speed change %)2
  Efficiency is power out divided by power in
  Maximum power is at 50% of no load speed
Mechanical Workshop

## Slide 15: Gear Boxes
Gear sets enclosed in a housing
Various gear ratios available
  Ratio is determined by the number of teeth on each gear
  Ratio = # Teeth Given Gear/ # Teeth Drive Gear
Used to reduce speed and increase torque
  Speed decrease based on the ratio
  Torque increases based on the ratio
Mechanical Workshop
Notes: Gear sets enclosed in a housing
Various gear ratios available
  Ratio is determined by the number of teeth on each gear
  Ratio = # Teeth Given Gear/ # Teeth Drive Gear
Used to reduce speed and increase torque
  Speed decrease based on the ratio
  Torque increases based on the ratio

## Slide 16: Gear Boxes (cont.)
Gear Boxes (cont)
  Most common is spur gear type
  Can install more than one motor
    More output power
    Increased output speed (for given torque)
  Approximately 95% efficiency (per gear set)
  Units are heavy, mount low in robot
  Can be back driven on output shaft
Mechanical Workshop

## Slide 17: Sprockets and Chains
Chain Size | Pitch | Average Ultimate Strength
#25 | 1/4” | 875 lb
#35 | 3/8” | 2100 lb
Sprockets and Chains
Note – Need to apply a safety factor, at least 1.5 or 2, to the average ultimate strength to obtain working strength
Mechanical Workshop

## Slide 18: Sprockets and Chains (cont.)
Center distance
  Minimum 30 times the pitch
  Generally 50 times the pitch
  Maximum 80 times the pitch
Provide center distance adjustment
Permissible chain speed (lubricated)
  #25 – 500 FPM
  #35 – 370 FPM
Wrap angle – approximately 120 degrees
Ratios – up to 3:1 (max of 5:1 for lower speed)
Mechanical Workshop

## Slide 19: Pneumatics
Cylinders
  Force = Pressure * Area
  Return stroke force is less (since area is less)
  Speed is controlled on the exhaust
  Generally used for two position moves
  Compressor used to compress atmospheric air pressure to elevated pressure
  Regulator used to reduce operation pressure (storage pressure is higher)
  Accumulators used to store air volume at elevated pressures
Mechanical Workshop

## Slide 20: Wheels
Basic
  Forward and backward motion
  Driven by one motor or multiple wheels connected to one motor
Mecanum
  Forward, backward, and side-strafing
  One motor per wheel
Mechanical Workshop

## Slide 21: SAFETY
SAFETY
  Wear your safety glasses when:
    Operating tools and machines
    Assembling robot
    Testing and operating robot
    At competition
  Operating machinery
    Read all instructions
    If you don’t know/understand, ASK
THINK and BE SAFE
Mechanical Workshop

## Slide 22: Robot
Mechanical Workshop

## Slide 23: Passing Mechanical Inspection
Meet rulebook requirements
  Weight
  Dimensions
  Bumpers
  Pressure requirements
  No sharp edges
Mechanical Workshop

## Slide 24: Lessons Learned
Read and understand the rules
Low center of gravity
Stronger
Faster
Voltage regulator
Layer design
Flexible shafts
Side drive wheels
Check lists
Know your strengths and sell them
Ability to measure distance
Tool belt with important tools
Mechanical Workshop